## Slide 1: An Introduction to Urban Land Use Change (ULC) Models
Prof. Yuji Murayama – Instructor
Wang Ruci – Teaching Assistant
Division of Spatial Information Science
University of Tsukuba

## Slide 2: Introduction
Urbanization is one of the most complex and dynamic processes of landscape changes.
Driving factors contributing to urban land changes (ULCs) are different spatiotemporally.
Recently, modeling ULCs with GIS and remote sensing has become a central component in urban geographical studies.

## Slide 3: Land Use Change Modeling
Describes the changes of land use and land cover over time.
Can be used to predict different scenarios of land use changes.
Uses currently available data or condition to combine with attributes (including population, economic, politics) and dynamic factors (including distance to water, distance to CBD, distance to road, etc.) to predict the future scenarios.

## Slide 4: ULC models enumeration……
CA
CLUE
CLUE-S
MARKOV
ABM
CEM
SD
LUSD
http://www.wisegeek.com/what-is-a-simulation-model.htm

## Slide 5: Continued
http://blog.sina.com.cn/s/blog_6352e4c40100pswc.html
1958
2010
2020
？
2030
？
2040
？

## Slide 6: Features of land use modeling
Level of analysis
Cross-scale dynamic
Driving factors
Spatial interaction and neighborhood effects
Temporal dynamics
Level of interaction

## Slide 7: Factors selected for ULC modeling
population
GDP
DEM
Slope
Environmental factors
Social factors

## Slide 8: Dynamic Factor Selection
Distance to…
http://www.innovativegis.com/basis/mapanalysis/Topic24/Topic24.htm

## Slide 9: Types of ULC models
Cellular Automation (CA) Model
A cellular automaton (CA) is a collection of cells arranged in a grid, such that each cell changes state as a function of time according to a defined set of rules that include the states of neighboring cells.
https://www.openabm.org/book/export/html/1949

## Slide 10: Continued
The conversation of land use and its effects (CLUE) model
The CLUE model is a dynamic, spatially explicit, land use and land cover change model.
http://www.ivm.vu.nl/en/Organisation/departments/spatial-analysis
-decision-support/Clue/

## Slide 11: Cont’d
Agent-Based Model(ABM)
An agent-based model is a computational model for simulating the actions and interactions of autonomous agent with a view to assessing their effects on the system.
http://jasss.soc.surrey.ac.uk/14/3/7.html

## Slide 12: Cont’d
Markov Model
A technique for predictive change modeling.
Predictions of future changes are based on the current condition.
http://www.slideshare.net/suj1thjay/markov-model-for-tmr-system-with-repair

## Slide 13: Continued
Land use scenarios dynamics model (LUSD Model)
The basic idea of LUSD is from SD model and CA model, both of which have statistical and spatial signification.
http://www.innovativegis.com/basis/mapanalysis/Topic8/Topic8.htm

## Slide 14: Continued
City expansion model in metropolitan area(CEM) model:
The CA model and Tietenberg model are composed to CEM model. It is an effective model to investigate the relationship between the urban expansion and population growth.
http://kungpao.tv/cem-vs-crm-which-platform-is-better/

## Slide 15: Model Selection
Model | Advantages | Disadvantages
CA Model | Statistical and spatial signification | Difficult to guarantee space resolution
CLUE Model (the conversation of land ) | Simulate multiple LULC change simultaneously | Invalid in the case without historical condition
MARKOV Model | Simulate the condition of T2 time point based on that of T1 | No spatial signification
LUSD Model (land use scenarios dynamics model) | Combine CA model and SD model Can do the factor analysis | Invalid for climate and resources factor analysis

## Slide 16: Conclusions
Projecting future states of land use and land cover is the precondition in numerical predictions about global changes. The current state of the ULC models is very useful for geographers, and using model to do LULC has good prospects for development.

## Slide 17: Reference
Focks D A, Daniels E, Haile D G, et al. A simulation model of the epidemiology of urban dengue fever: literature analysis, model development, preliminary validation, and samples of simulation results. American Journal of Tropical Medicine and Hygiene, 1995, 53(5): 489-506.
Waddell P. UrbanSim. Modeling urban development for land use, transportation, and environmental planning. Journal of the American Planning Association, 2002, 68(3): 297-314.
Stephenne N, Lambin E F. A dynamic simulation model of land-use changes in Sudano-sahelian countries of Africa. Agriculture, ecosystems & environment, 2001, 85(1): 145-161.
White R, Engelen G, Uljee I. The use of constrained cellular automata for high-resolution modelling of urban land-use dynamics. Environment and Planning B: Planning and Design, 1997, 24(3): 323-343.